## Slide 1
EmbedSim Architecture
Python · Cython · C Code Generation · FMU / Modelica
①
Simulation Engine
DFS block graph
topological sort
ODE integration
②
Code Generation
StepGenerator emits
MISRA C:2012
EmbedSim_step.c/h
③
FMU / Modelica
Physics plant models
OpenModelica + FMPy
co-simulation
④
Cython Bridge
float[::1] zero-copy
PYXInspector metadata
build pipeline
MISRA C:2012 · ISO 26262 ASIL-D · AURIX TC3xx · ARM Cortex-M · Open Source

## Slide 2
Simulation Engine
① Block Graph Wiring (>> operator)
sin_src >> loop_sum >> loop_gain >> loop_out
Connects successors/inputs lists. No computation — pure Python object graph.
② Two-Pass DFS (topological sort)
Pass 1: find_loop_breakers() — collect LoopBreaker subclasses (VectorDelay) into a set.
Pass 2: DFS post-order — back-edge on LoopBreaker cuts the loop; back-edge on normal block raises ValueError.
③ Runtime _compute_all_blocks()
Iterates blocks_order once per step. LoopBreakers output y(k−1) before their upstream runs. Missing outputs fall back to [0.0] — warning at t=0 only.
DFC Execution Order
1
motor_delay
LoopBreaker z⁻¹
2
ctrl_packer
Pack 8-signal bus
3
cg_start
CodeGen boundary
4
dfc
DFC controller
5
svpwm_pack
Pack v_α / v_β
6
svpwm
SVPWM duties
7
cg_end
CodeGen boundary
8
motor
PMSM plant
ODE Solvers
EULER
1st-order
1× cost
HEUN
2nd-order
2× cost ← default
RK4
4th-order
4× cost

## Slide 3
FMU / Modelica — Physics Plant Layer
1. Write .mo
Modelica dq-frame
equations + FMI 2.0
connectors
2. Compile → .fmu
ZIP: modelDescription
.xml + binaries/*.so
+ resources/*.bin
3. gen_fmu.py
Reads .xml, emits
VectorBlock Python
wrapper class
4. FMUBlock
set_real → do_step
→ get_real per tick
via FMPy
5. C_CODEGEN
_EXCLUDE
Plant never enters
StepGenerator —
sim-only artifact
modelDescription.xml → VectorBlock
causality=input
duty_a/b/c, v_dc, T_load
FMUBlock.INPUT_VARS
causality=output
rpm, ia, ib, ic, theta_m …
FMUBlock.OUTPUT_VARS
causality=parameter
R, L_d, L_q, λ_pm, J, p …
FMUBlock.DEFAULT_PARAMS
Real start=
0.19, 1.25e-4, 0.0014 …
DEFAULT_PARAMS values
PMSM_Python_Plant — Portable Fallback
When FMU binary is unavailable
(different OS, ARM target, unit testing)
Pure-Python RK4 integration of dq-frame PMSM equations.
Same 8-element output bus:
[ rpm, ia, ib, ic, theta_m, T_em, id, iq ]
Key design:
All coordinate transforms delegate to coordinate_transform_blocks.py — the same Python mirrors of the canonical C functions. No inline transform math.

## Slide 4
Code Generation — StepGenerator
1. DFS collect
Backward from
cg_end → cg_start
ordered block list
2. emit #includes
C_HEADERS[i].lower()
per block,
deduplicated set
3. emit structs
EmbedSim_Input_T
EmbedSim_Output_T
from *_NAMES attrs
4. emit Init()
static state vars
C_INIT_ARGS → typed
f-suffix literals
5. emit Step()
_emit_block() for
each block in
topological order
_emit_block() Decision Tree
P1
C_CUSTOM_EMIT set
Verbatim C — non-standard ABI (e.g. DFC voltage normalisation)
P2
IS_UNIT_DELAY
memcpy from z⁻¹ register (VectorDelay)
P3
NUM_INPUTS == 0
Source: Step(&state, dt, y) no u[] needed
P4
step_func set
Normal: build u[], call Step(&state, u, dt, y)
P5
C_SOURCES, no step_func
TODO comment — block is incomplete
C Name Derivation (every name is mechanical)
State var
block.name + "_state"
dfc_state
Output buf
"y_" + block.name
y_dfc
Input buf
"u_" + block.name
u_svpwm_pack
Init() call
init_func + C_INIT_ARGS values
DFC_Controller_Init
(&dfc_state, 0.00005000f)
#include
C_HEADERS[i].lower()
embed_sim_dfc
_controller.h
DT macro
1.0/dt_hz → .8f + 'f'
EMBEDSIM_DT
(0.00005000f)
MISRA: Rule 7.2 — f suffix on all float literals · Rule 8.7 — static linkage for file-scope state · Rule 15.5 — single return